## Slide 1: EEG denoising

## Slide 2: Problem
Removing artifacts from EEG signals with minimum distortion and contamination
  enhance the BCI performance
  increase the accuracy of data interpretation
  enhance classification models performance

## Slide 3: Types of artifacts
Eye blinks
https://www.learningeeg.com/artifacts

## Slide 4: Types of artifacts
Eye blinks
Lateral eye movements
https://www.learningeeg.com/artifacts

## Slide 5: Types of artifacts
Eye blinks
Lateral eye movements
Chewing and tongue artifact
https://www.learningeeg.com/artifacts

## Slide 6: Types of artifacts
Eye blinks
Lateral eye movements
Chewing and tongue artifact
ECG artifact
Electrical artifact
https://www.learningeeg.com/artifacts

## Slide 7: Types of artifacts
Eye blinks
Lateral eye movements
Chewing and tongue artifact
ECG artifact
Electrical artifact
Myogenic artifact
https://www.learningeeg.com/artifacts

## Slide 8: Types of artifacts
Eye blinks
Lateral eye movements
Chewing and tongue
ECG
Electrical
Myogenic
Sweat
https://www.learningeeg.com/artifacts

## Slide 9: Approaches
Blind source separation (BSS) methods
Artifact subspace reconstruction (ASR)
Independent component analysis (ICA)
ML/DL
Residual CNN
Autoencoder
UNet
GAN
Transfomer

## Slide 10: Approaches
Blind source separation (BSS) methods
Artifact subspace reconstruction (ASR)
Independent component analysis (ICA)
ML/DL
Residual CNN
Autoencoder
UNet
GAN
Transfomer
Use statistical assumptions
Single nonlinear/linear mapping function, might be too simplistic
Not fully automated

## Slide 11: Deep Convolutional Autoencoder (DAE)
F. Lopes et al., "Automatic Electroencephalogram Artifact Removal Using Deep Convolutional Neural Networks," in IEEE Access, vol. 9, pp. 149955-149970, 2021, doi: 10.1109/ACCESS.2021.3125728.

## Slide 12: Deep Convolutional Autoencoder (DAE)
F. Lopes et al., "Automatic Electroencephalogram Artifact Removal Using Deep Convolutional Neural Networks," in IEEE Access, vol. 9, pp. 149955-149970, 2021, doi: 10.1109/ACCESS.2021.3125728.
Data
  19 channels
  128 Hz
  chunk length 7680 (60 s)
  normalization

## Slide 13: Deep Convolutional Autoencoder (DAE)
F. Lopes et al., "Automatic Electroencephalogram Artifact Removal Using Deep Convolutional Neural Networks," in IEEE Access, vol. 9, pp. 149955-149970, 2021, doi: 10.1109/ACCESS.2021.3125728.

## Slide 14: Deep Convolutional Autoencoder (DAE)
F. Lopes et al., "Automatic Electroencephalogram Artifact Removal Using Deep Convolutional Neural Networks," in IEEE Access, vol. 9, pp. 149955-149970, 2021, doi: 10.1109/ACCESS.2021.3125728.

## Slide 15: 1D-ResCNN
Sun, W., Su, Y., Wu, X., Wu, X., 2020. A novel end-to-end 1D-ResCNN model to remove artifact from EEG signals. Neurocomputing 404, 108–121.

## Slide 16: 1D-ResCNN
Data
  256 Hz
  window size of 400, stride 380 (~1.56 s)
  normalization
Sun, W., Su, Y., Wu, X., Wu, X., 2020. A novel end-to-end 1D-ResCNN model to remove artifact from EEG signals. Neurocomputing 404, 108–121.

## Slide 17: 1D-ResCNN
Sun, W., Su, Y., Wu, X., Wu, X., 2020. A novel end-to-end 1D-ResCNN model to remove artifact from EEG signals. Neurocomputing 404, 108–121.

## Slide 18: IC-U-Net
Chun-Hsiang Chuang, Kong-Yi Chang, Chih-Sheng Huang, Tzyy-Ping Jung, IC-U-Net: A U-Net-based Denoising Autoencoder Using Mixtures of Independent Components for Automatic EEG Artifact Removal, NeuroImage, Volume 263, 2022, 119586, ISSN 1053-8119,

## Slide 19: IC-U-Net
Data
  30 channels
  256 Hz
  chunk length 1024 (4 s)
  normalization
Chun-Hsiang Chuang, Kong-Yi Chang, Chih-Sheng Huang, Tzyy-Ping Jung, IC-U-Net: A U-Net-based Denoising Autoencoder Using Mixtures of Independent Components for Automatic EEG Artifact Removal, NeuroImage, Volume 263, 2022, 119586, ISSN 1053-8119,

## Slide 20: IC-U-Net
Results
Chun-Hsiang Chuang, Kong-Yi Chang, Chih-Sheng Huang, Tzyy-Ping Jung, IC-U-Net: A U-Net-based Denoising Autoencoder Using Mixtures of Independent Components for Automatic EEG Artifact Removal, NeuroImage, Volume 263, 2022, 119586, ISSN 1053-8119,

## Slide 21: IC-U-Net
Results
Chun-Hsiang Chuang, Kong-Yi Chang, Chih-Sheng Huang, Tzyy-Ping Jung, IC-U-Net: A U-Net-based Denoising Autoencoder Using Mixtures of Independent Components for Automatic EEG Artifact Removal, NeuroImage, Volume 263, 2022, 119586, ISSN 1053-8119,

## Slide 22: EEGDnet transformer
Yi, Peng & Chen, Kecheng & Ma, Zhaoqi & Zhao, Di & Pu, Xiaorong & Ren, Yazhou. (2021). EEGDnet: Fusing Non-Local and Local Self-Similarity for 1-D EEG Signal Denoising with 2-D Transformer.

## Slide 23: EEGDnet transformer
Data
  EEGDnet dataset
  No channels
  256 Hz
  epoch length 512 (2 seconds)
  4514 EEG epochs
  3400 ocular artifact epochs
  5598 muscle artifact epochs
  Mixed signals are generated via y = x + λn with a uniformly distributed SNR from -7dB to 2d (x10 to dataset size)
Yi, Peng & Chen, Kecheng & Ma, Zhaoqi & Zhao, Di & Pu, Xiaorong & Ren, Yazhou. (2021). EEGDnet: Fusing Non-Local and Local Self-Similarity for 1-D EEG Signal Denoising with 2-D Transformer.

## Slide 24: EEGDnet transformer
Yi, Peng & Chen, Kecheng & Ma, Zhaoqi & Zhao, Di & Pu, Xiaorong & Ren, Yazhou. (2021). EEGDnet: Fusing Non-Local and Local Self-Similarity for 1-D EEG Signal Denoising with 2-D Transformer.

## Slide 25: Models evaluation

## Slide 26: Dataset
Data
  EEGDnet dataset
  No channels
  256 Hz
  epoch length 512 (2 seconds)
  4514 EEG epochs
  3400 ocular artifact epochs
  5598 muscle artifact epochs
  Mixed signals are generated via y = x + λn with a uniformly distributed SNR from -7dB to 2d (x10 to dataset size)
Zhang, H.; Zhao, M.; Wei, C.; Mantini, D.; Li, Z.; and Liu, Q. 2020. EEGdenoiseNet: A benchmark dataset for deep learning solutions of EEG denoising. arXiv preprint arXiv:2009.11662.

## Slide 27
Zhang, H.; Zhao, M.; Wei, C.; Mantini, D.; Li, Z.; and Liu, Q. 2020. EEGdenoiseNet: A benchmark dataset for deep learning solutions of EEG denoising. arXiv preprint arXiv:2009.11662.

## Slide 28
Zhang, H.; Zhao, M.; Wei, C.; Mantini, D.; Li, Z.; and Liu, Q. 2020. EEGdenoiseNet: A benchmark dataset for deep learning solutions of EEG denoising. arXiv preprint arXiv:2009.11662.

## Slide 29: Dataset
Dataset
  4514 EEG epochs
  3400 ocular artifact epochs
  5598 muscle artifact epochs
  Mixed signals are generated via y = x + λn with a uniformly distributed SNR from -7dB to 2d (x10 to dataset size)
  Resulting size of dataset (80/10/10 split):
    EOG: train=27200, validation=3400, test=3400
    EMG: train=36112, validation=4514, test=4514
Zhang, H.; Zhao, M.; Wei, C.; Mantini, D.; Li, Z.; and Liu, Q. 2020. EEGdenoiseNet: A benchmark dataset for deep learning solutions of EEG denoising. arXiv preprint arXiv:2009.11662.

## Slide 30
EOG
EMG

## Slide 31: Results
 | EOG MSE | EOG SNR, db | EOG CC | EMG MSE | EMG SNR, db | EMG CC
1D-ResCNN | 40.643 | 11.405 | 0.965 | 78.022 | 8.369 | 0.929
IC-U-Net | 5.791 | 20.523 | 0.995 | 17.296 | 14.947 | 0.986
EEGDnet transformer | 22.236 | 14.467 | 0.979 | 57.739 | 9.861 | 0.943

## Slide 32: EOG example

## Slide 33: EOG example

## Slide 34: EMG example

## Slide 35: EMG example

## Slide 36: Amount of parameters
model | trainable | total
1D-ResCNN | 325891 | 325891
IC-U-Net | 2777943 | 2777943
EEGDnet transformer | 675398 | 675398

## Slide 37: Conclusion
IC-U-Net outperformed 1D-ResCNN and EEGDnet transformer architectures in training during 50 epochs;
There is a lack of public dataset containing information about channels;
Тone of the considered models use relationships between channels in their architecture, which can be useful.

## Slide 38: Training
batch size: 128
optimizer: AdamW(lr=1e-3)
scheduler: ReduceLROnPlateau(factor=0.5, patience=3)
number of epochs: 50